## Slide 1: Exploring Semantic Reverse Engineering for Software Binary Protection
Pengfei Sun
Thesis advisor: Prof. Saman Zonouz
Committee Members: Prof. Ivan Marsic, Prof. Sheng Wei
and Dr. Praveen K. Murthy*
* Fujitsu Labs of America

## Slide 2: Outline
Introduction
Trace-free memory data structure forensics
Reversing semantics of embedded IoT software binaries
Case-study: data attacks against power system operations
Known vulnerability detection for Mobile/IoT firmware
Conclusion

## Slide 3: Outline
Introduction
Trace-free memory data structure forensics
Reversing semantics of embedded IoT software binaries
Case-study: data attacks against power system operations
Known vulnerability detection for Mobile/IoT firmware
Conclusion

## Slide 4: Software is Everywhere

## Slide 5: Internet of Things (IoT) connected devices installed base worldwide from 2015 to 2025 (in billions)
Chart: 
| 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025
Connected devices in billions | 15.41 | 17.68 | 20.35 | 23.14 | 26.66 | 30.73 | 35.82 | 42.62 | 51.11 | 62.12 | 75.44
Source: IHS ID 471264

## Slide 6: Some Facts About Software
Society increasingly relies on software
  … but it is unreliable and low quality
Maintenance is always essential
  … but large amount embedded software is rarely updated
Bug

## Slide 8
unsigned int foo(
char *buf,
unsigned int *out)
{
unsigned int c;
c = 0;
if (buf) {
*out = strlen(buf);
c = *out - 1;
}
return c;
}
Compile and Link
Strip

## Slide 9: Software Reverse Engineering
Reverse Engineering
Assembly code
Control Flow Graph (CFG)

## Slide 10: Semantic Reverse Engineering
Semantic Reverse Engineering
Data Structure:
Definition
Memory instances
Algorithm:
Control algorithm

## Slide 11: Three Challenges
HOW TO recognize and recover data structure instances from a memory image without execution traces.
HOW TO locate the critical control algorithm implementation and extract the semantic meaning for the associated memory addresses/registers.
HOW TO leverage semantic reverse engineering for vulnerability detection.

## Slide 12: Outline
Introduction
Trace-free memory data structure forensics
Reversing semantics of embedded IoT software binaries
Case-study: data attacks against power system operations
Known vulnerability detection for Mobile/IoT firmware
Conclusion
Pengfei Sun, Rui Han, Mingbo Zhang, Saman Zonouz, Trace-Free Memory Data Structure Forensics via Past Inference and Future Speculations. Annual Computer Security Applications Conference (ACSAC), 2016.

## Slide 13: Motivation
field type
Data structure 1
field type
field type
field type
Data structure 2
field type
field type
field type
field type
Data structure 3
Memory forensics
Vulnerability
discovery
Malware
analysis

## Slide 14: Previous Work
Laika (OSDI’08)
SigGraph (NDSS’11)
Reward (NDSS’10)
TIE (NDSS’11)
Howard (NDSS’11)
Aggregated structure pattern
Only kernel,
Source code
Need execution trace,
High overhead
Correct data structure
Stripped binary code
No execution trace,
Low overhead
Limitations
My approach

## Slide 15: ReViver
...
09406ca0 0000 0000 0021 0000 6004 0940 6d00 0940
09406cb0 0000 0000 efef efef fefe fefe 0018 0000
...
09407570 acfc b76f 0e7f af6f efef efef fefe fefe
09407580 0014 0000 0039 0000 0000 0000 0004 0000
...
service_library {
const char *
void *
struct service_library *
}
known_function {
const char *
void *
}
Part of memory dump

## Slide 16: ReViver
Present: static memory analysis
Past: statistical information
Future: speculative forensics

## Slide 17: Present: Static Memory Analysis
...
09406ca0 0000 0000 0021 0000 6004 0940 6d00 0940
09406cb0 0000 0000 efef efef fefe fefe 0018 0000
...
09407570 acfc b76f 0e7f af6f efef efef fefe fefe
09407580 0014 0000 0039 0000 0000 0000 0004 0000
...
Memory initial layout
Suspension point
Part of memory dump

## Slide 18: Present: Static Memory Analysis
...
09406ca0 0000 0000 0021 0000 6004 0940 6d00 0940
09406cb0 0000 0000 efef efef fefe fefe 0018 0000
...
09407570 acfc b76f 0e7f af6f efef efef fefe fefe
09407580 0014 0000 0039 0000 0000 0000 0004 0000
...
Trace-free reverse engineering
  No need for execution tracing
  Memory allocation function hooking (1.8% runtime overhead)
    Landmarks (efef efef fefe fefe )
  Superset of possible types for each memory region
    String, pointer-to-pointers, data structure, str-zeros
Landmarks
Size is 0x18
Pointer address: 0x09406ca8
stru_0x9406ca8 {
pointer-str
pointer-stru
zero
}
Part of memory dump

## Slide 19: Past: Statistical Information
Entry
Suspend
Collecting statistical information
  Completed symbolic execution
  Best-effort partial symbolic execution
    Relevant execution paths
    Partial and directed

## Slide 20: Future: Speculative Forensics
Suspend
Exit
Type sink
(e.g., library/ system calls and floating point instructions)
Backward taint analysis
...
09406ca0 0000 0000 0021 0000 6004 0940 6d00 0940
09406cb0 0000 0000 efef efef fefe fefe 0018 0000

## Slide 21: Case Study: CoreUtils Groups
...
09406ca0 0000 0000 0021 0000 6004 0940 6d00 0940
09406cb0 0000 0000 efef efef fefe fefe 0018 0000
...
09407570 acfc b76f 0e7f af6f efef efef fefe fefe
09407580 0014 0000 0039 0000 0000 0000 0004 0000
09407590 0018 0000 001b 0000 001e 0000 002e 0000
094075a0 006d 0000 007c 0000 03e8 0000 efef efef
094075b0 fefe fefe 0030 0000 0000 0000 ea49 0001
094075c0 0000 0000 0000 0000 0000 0000 0000 0000
094075d0 0000 0000 0000 0000 0000 0000 0000 0000
094075e0 0000 0000 0000 0000 0000 0000 0000 0000
094075f0 0000 0000 a980 b76e ffff ffff 0041 0000
09407600 0000 0000 0000 0000 7658 0940 ffff ffff
09407610 ffff ffff 0000 0000 7664 0940 0000 0000
09407620 0000 0000 ffff ffff ffff ffff 0000 0000
09407630 0000 0000 0000 0000 0000 0000 0000 0000
09407640 0000 0000 0000 0000 0000 0000 0000 0000
09407650 0000 0000 9a20 b76e 0000 0000 ffff ffff
09407660 0000 0000 0000 0000 0000 0000 0000 0000
09407670 0000 0000 0000 0000 0000 0000 0000 0000
09407680 0000 0000 0000 0000 0000 0000 0000 0000
09407690 0000 0000 0000 0000 0000 0000 0000 0000
094076a0 0000 0000 0000 0000 0000 0000 0000 0000
094076b0 0000 0000 0000 0000 0000 0000 0000 0000
094076c0 0000 0000 0000 0000 0000 0000 0000 0000
094076d0 0000 0000 0000 0000 0000 0000 0000 0000
094076e0 0000 0000 98a0 b76e efef efef fefe fefe
This case study will show how ReViver use the hybrid solution to get memory data structure layout.

## Slide 22: Case Study: CoreUtils Groups
...
09406ca0 0000 0000 0021 0000 6004 0940 6d00 0940
09406cb0 0000 0000 efef efef fefe fefe 0018 0000
...
service_library {
const char *
void *
struct service_library *
}
stru_0x9406CA8 {
pointer-str
pointer-stru
zero
}
Database
libname_list {
const char *
struct libname_list *
int
}

## Slide 23: Case Study: CoreUtils Groups
...
09406ca0 0000 0000 0021 0000 6004 0940 6d00 0940
09406cb0 0000 0000 efef efef fefe fefe 0018 0000
...
09407570 acfc b76f 0e7f af6f efef efef fefe fefe
09407580 0014 0000 0039 0000 0000 0000 0004 0000
09407590 0018 0000 001b 0000 001e 0000 002e 0000
094075a0 006d 0000 007c 0000 03e8 0000 efef efef
094075b0 fefe fefe 0030 0000 0000 0000 ea49 0001
094075c0 0000 0000 0000 0000 0000 0000 0000 0000
094075d0 0000 0000 0000 0000 0000 0000 0000 0000
094075e0 0000 0000 0000 0000 0000 0000 0000 0000
094075f0 0000 0000 a980 b76e ffff ffff 0041 0000
09407600 0000 0000 0000 0000 7658 0940 ffff ffff
09407610 ffff ffff 0000 0000 7664 0940 0000 0000
09407620 0000 0000 ffff ffff ffff ffff 0000 0000
09407630 0000 0000 0000 0000 0000 0000 0000 0000
09407640 0000 0000 0000 0000 0000 0000 0000 0000
09407650 0000 0000 9a20 b76e 0000 0000 ffff ffff
09407660 0000 0000 0000 0000 0000 0000 0000 0000
09407670 0000 0000 0000 0000 0000 0000 0000 0000
09407680 0000 0000 0000 0000 0000 0000 0000 0000
09407690 0000 0000 0000 0000 0000 0000 0000 0000
094076a0 0000 0000 0000 0000 0000 0000 0000 0000
094076b0 0000 0000 0000 0000 0000 0000 0000 0000
094076c0 0000 0000 0000 0000 0000 0000 0000 0000
094076d0 0000 0000 0000 0000 0000 0000 0000 0000
094076e0 0000 0000 98a0 b76e efef efef fefe fefe
exit: malloc
ret: 0x094075c0
enter: fgetpos(0x094075c0, 0xbfdcbbb4)
definition: fgetpos(_IO_FILE *, fpost_t *)
_IO_FILE

## Slide 24: Case Study: CoreUtils Groups
...
09406ca0 0000 0000 0021 0000 6004 0940 6d00 0940
09406cb0 0000 0000 efef efef fefe fefe 0018 0000
...
09407570 acfc b76f 0e7f af6f efef efef fefe fefe
09407580 0014 0000 0039 0000 0000 0000 0004 0000
09407590 0018 0000 001b 0000 001e 0000 002e 0000
094075a0 006d 0000 007c 0000 03e8 0000 efef efef
094075b0 fefe fefe 0030 0000 0000 0000 ea49 0001
094075c0 0000 0000 0000 0000 0000 0000 0000 0000
094075d0 0000 0000 0000 0000 0000 0000 0000 0000
094075e0 0000 0000 0000 0000 0000 0000 0000 0000
094075f0 0000 0000 a980 b76e ffff ffff 0041 0000
09407600 0000 0000 0000 0000 7658 0940 ffff ffff
09407610 ffff ffff 0000 0000 7664 0940 0000 0000
09407620 0000 0000 ffff ffff ffff ffff 0000 0000
09407630 0000 0000 0000 0000 0000 0000 0000 0000
09407640 0000 0000 0000 0000 0000 0000 0000 0000
09407650 0000 0000 9a20 b76e 0000 0000 ffff ffff
09407660 0000 0000 0000 0000 0000 0000 0000 0000
09407670 0000 0000 0000 0000 0000 0000 0000 0000
09407680 0000 0000 0000 0000 0000 0000 0000 0000
09407690 0000 0000 0000 0000 0000 0000 0000 0000
094076a0 0000 0000 0000 0000 0000 0000 0000 0000
094076b0 0000 0000 0000 0000 0000 0000 0000 0000
094076c0 0000 0000 0000 0000 0000 0000 0000 0000
094076d0 0000 0000 0000 0000 0000 0000 0000 0000
094076e0 0000 0000 98a0 b76e efef efef fefe fefe
Name | Size
0x94075C0 | 0x160
_IO_FILE | 0x94
locked_FILE | 0x160

## Slide 25: Accuracy
Accuracy: how many data structure instances have been recognized and recovered from memory image?
ReViver’s overall accuracy is 98.1%

## Slide 26: Three Challenges
HOW TO recognize and recover data structure instances from a memory image without execution traces.
HOW TO locate the critical control algorithm implementation and extract the semantic meaning for the associated memory addresses/registers.
HOW TO leverage semantic reverse engineering for vulnerability detection.

## Slide 27: Outline
Introduction
Trace-free memory data structure forensics
Reversing semantics of embedded IoT software binaries
Case-study: data attacks against power system operations
Known vulnerability detection for Mobile/IoT firmware
Conclusion
Pengfei Sun, Luis Garcia and Saman Zonouz, Tell Me More Than Just Assembly! Reversing Semantics of Embedded IoT and Industrial Control Software Binaries. The 49th IEEE/IFIP International Conference on Dependable Systems and Networks (DSN 2019), 2019.

## Slide 28: Control Algorithm
Proportional-Integral-Derivate (PID) controllers are used in programmable logic controller (PLC) programs
Kalman-Filters for guidance, navigation and control of drones
Pulse-width modulation (PWM) is used for robotics and 3D printer extruder motor control

## Slide 29: Motivation Example

## Slide 30: Current Solutions
BinDiff (SSTIC'05)
BinJuice (PPREW '13)
Blex (Usenix’14)
Reward (NDSS’10)
TIE (NDSS’11)
Howard (NDSS’11)
ReViver (ACSAC’16)
IDA PRO
OllyDbg
Ninja
Snowman
Disassembler,
Decompiler,
Static and dynamic analysis
Data structure definition,
Data structure memory instance
Binary similarity checking

## Slide 31: My Solution
Propose a domain-specific reverse engineering solution to extract high-level algorithmic control- and data-flow semantics from embedded binary executables in IoT and ICS applications.
Introduce a semantic mapping using dynamic binary analysis and symbolic comparison of the mathematical and binary expressions to fill the semantic gap between high-level algorithm descriptions and low-level stripped binary segments.

## Slide 32
Mismo Overview
Binary executable
Algorithm
ICS/IoT Device
Controller Code
(binary executable)
Control Algorithm’s Subroutine Identification
CFG Refinement
Symbolic Controller
Abstract Syntax Trees
ICS/IoT
Control Algorithms
Algorithmic Mathematical
Abstract Syntax Trees

## Slide 33
Algorithmic Mathematical
Abstract Syntax Trees
Formal Symbolic
Equivalence Check
Annotated
Disassembly
Mismo Overview
Symbolic Controller
Abstract Syntax Trees

## Slide 34
Mismo Overview
ICS/IoT Device
Controller Code
(binary executable)
Control Algorithm’s Subroutine Identification
CFG Refinement
Symbolic Controller
Abstract Syntax Trees
ICS/IoT
Control Algorithms
Algorithmic Mathematical
Abstract Syntax Trees
Formal Symbolic
Equivalence Check

## Slide 35
Case Study
ICS/IoT Device
Controller Code
(binary executable)
Control Algorithm’s Subroutine Identification
CFG Refinement
Symbolic Controller
Abstract Syntax Trees
ICS/IoT
Control Algorithms
Algorithmic Mathematical
Abstract Syntax Trees
Formal Symbolic
Equivalence Check
Chart: Functions
| sub_B7C8 | sub_9E14 | sub_A0C8 | sub_A020 | sub_9544 | sub_9288 | sub_9CA8 | sub_9BF8 | sub_8E10 | sub_8D68 | sub_8D68 | sub_9CA8 | sub_9BF8 | sub_8E10 | sub_8D68 | sub_8D68 | sub_8D68 | sub_8D68 | sub_10288 | sub_1024C | sub_94F8 | sub_8EC4 | sub_FBDC | sub_FBFC | sub_EB08 | sub_EB08 | sub_950C | sub_9158
Value_based Taint | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 15 | 0 | 15 | 15 | 0 | 0 | 0 | 0 | 0 | 0
Taint analysis
Arithmetic operations

## Slide 36
Case Study
ICS/IoT Device
Controller Code
(binary executable)
Control Algorithm’s Subroutine Identification
CFG Refinement
Symbolic Controller
Abstract Syntax Trees
ICS/IoT
Control Algorithms
Algorithmic Mathematical
Abstract Syntax Trees
Formal Symbolic
Equivalence Check
36
Errors checking,
Value range checking

## Slide 37
Case Study
ICS/IoT Device
Controller Code
(binary executable)
Control Algorithm’s Subroutine Identification
CFG Refinement
Symbolic Controller
Abstract Syntax Trees
ICS/IoT
Control Algorithms
Algorithmic Mathematical
Abstract Syntax Trees
Formal Symbolic
Equivalence Check

## Slide 38
Backward value analysis
Case Study
Symbolic Controller
Abstract Syntax Trees
Symbolic expression
Symbolic execution
Symbolic
output
variable
Symbolic
input
variables
…
0x90DE: VMUL.F64 D6, D6, D7
-> 0xc0175999f54482ee
0x90E2: VLDR D7, [R7,#0x3C+var_2C]
-> 0x4028000000000000
0x90E6: VADD.F64 D7, D6, D7
-> 0x4018a6660abb7d12
…
Backward slicing analysis

## Slide 39
Case Study
Symbolic Controller
Abstract Syntax Trees
Symbolic expression
((((Sym_15 ∗ (((Sym_12 ∗ Sym_11) ∗ Sym_13) + Sym_14)) / ((Sym_19 ∗ (Sym_15 ∗ (((Sym_12 ∗ Sym_11) ∗ Sym_13) + Sym_14))) + Sym_16)) ∗ ((((Sym_7) ^ (-1) ∗ Sym_8) + ((Sym_5 ∗ (((Sym_3) ^ (-1) ∗ Sym_4) + ((Sym_0 ∗ Sym_1) + (Sym_18 ∗ Sym_2)))) + (Sym_18 ∗ Sym_6))) − ((Sym_19 ∗ ((Sym_18 ∗ Sym_10) + (Sym_11∗ Sym_9))) + (Sym_17 ∗ Sym_18)))) + ((Sym_18 ∗ Sym_10) + (Sym_11 ∗ Sym_9)))

## Slide 40
Case Study
Symbolic Controller
Abstract Syntax Trees

## Slide 41
Case Study
Algorithmic Mathematical
Abstract Syntax Trees

## Slide 42
Formal Symbolic
Equivalence Check
Mismo Overview
Sym_3 -> Q
Sym_7 -> R
…

## Slide 43: Annotated Disassembly

## Slide 44: Evaluation
Accuracy
Data: the portion of resolved symbolic variables
Code: the portion of resolved instructions

## Slide 45: Compare with Snowman (decompiler)

## Slide 46: Linux Kernel Bug
…
/* compute intermediate PID terms */
p_term = -p_param.kp * (xk - xk_1);
i_term = p_param.kp * p_param.ki * p_param.ts * ek;
d_term = -p_param.kp * p_param.kd * (xk - 2 * xk_1
+xk_2) / p_param.ts;
/* compute output */
*yk += p_term + i_term + d_term;
…
Mismo
Algorithm
Program Code

## Slide 47: Outline
Introduction
Trace-free memory data structure forensics
Reversing semantics of embedded IoT software binaries
Case-study: data attacks against power system operations
Known vulnerability detection for Mobile/IoT firmware
Conclusion
Devendra Shelar, Pengfei Sun, Saurabh Amin, Saman Zonouz, Compromising Security of Economic Dispatch in Power System Operations. The 47th IEEE/IFIP International Conference on Dependable Systems and Networks (DSN 2017), 2017.

## Slide 48: Attack Target
Control algorithm (e.g. Optimal Power Flow)

## Slide 49: Physics-aware memory attack on control systems
Power System
…
…
sensors
actuators
Cyber
Physical
Controller Software
measurements
control commands
control loop
memory control
data corruption

## Slide 50: My Approach
Adversary-optimal value calculation for modifiable parameters
Control-sensitive parameters (memory values) that can be detected and modified by the attack
Runtime attack: control-sensitive data location and corruption
Offline controller software analysis and memory pattern extraction
Malicious values for control-sensitive parameters

## Slide 51: Logical memory structural patterns
Logical memory structural patterns
Intra-class type patterns
Code pointer-instruction patterns
Data pointer-based patterns

## Slide 52: PowerWorld pre-attack system state
06410AE0 0001 0000 65C0 0949 0000 0000 0000 0000
06410AF0 0000 0000 0000 0000 0000 0000 FE00 0000
06410B00 0000 0000 0000 0000 0001 0000 0000 0000
06410B10 0000 0000 0000 3FC0 FAE1 42C7 FAE1 42C7
06410840 0001 0000 64A0 0949 0000 0000 0000 0000
06410850 0000 0000 0000 0000 0000 0000 FE00 0000
06410860 0000 0000 0000 0000 0001 0000 0000 0000
06410870 0000 0000 0000 3FC0 FAE1 42C7 FAE1 42C7
Generator
Bus
Transmission line

## Slide 53: PowerWorld post-attack system state
06410AE0 0001 0000 65C0 0949 0000 0000 0000 0000
06410AF0 0000 0000 0000 0000 0000 0000 FE00 0000
06410B00 0000 0000 0000 0000 0001 0000 0000 0000
06410B10 0000 0000 999A 4019 FAE1 42C7 FAE1 42C7
06410840 0001 0000 64A0 0949 0000 0000 0000 0000
06410850 0000 0000 0000 0000 0000 0000 FE00 0000
06410860 0000 0000 0000 0000 0001 0000 0000 0000
06410870 0000 0000 999A 3F99 FAE1 42C7 FAE1 42C7

## Slide 54: Three Challenges
HOW TO recognize and recover data structure instances from a memory image without execution traces.
HOW TO locate the critical control algorithm implementation and extract the semantic meaning for the associated memory addresses/registers.
HOW TO leverage semantic reverse engineering for vulnerability detection.

## Slide 55: Outline
Introduction
Trace-free memory data structure forensics
Reversing semantics of embedded IoT software binaries
Case-study: data attacks against power system operations
Known vulnerability detection for Mobile/IoT firmware
Conclusion
Pengfei Sun, Luis Garcia, Saman Zonouz, I Know What You Didn't Do Last Vulnerability! Firmware Analysis via Deep Learning for Known Security Vulnerabilities. The 26th ACM Conference on Computer and Communications Security (CCS’19), 2019, to be submitted.

## Slide 58
07/2016 so far
~ 2,076 REPORTED Vulnerabilities
only in Android

## Slide 59
  Patches are handed down a long chain, e.g., four parties for Android user (OS vendor  Chipset vendor  Phone vendor  Carrier)
  Only some devices get pathed, even these “full patched” are still missing some patches
Hidden patch gap

## Slide 60: Automate the known vulnerability detection in Mobile/IoT?

## Slide 61: Objectives
Mobile/IoT
Firmware

## Slide 62: Challenges for Vulnerability Detection
No source code available
No cooperation from device vendors
No cooperation from firmware developers
x86
ARM
Cross-Platform
Similar or not similar? It’s a problem!
Automation &
Scalability

## Slide 63: Previous Work
Genius(CCS’16)
Gemini(CCS’17)
BinDiff (SSTIC'05)
BinJuice (PPREW '13)
Blex (Usenix’14)
Discovre (NDSS’16)
FIBER(Usenix’18)
Ccfinder (IEEE’02)
Deckard(IEEE’07)
Soure code
Binary,
Only Static or dynamic analysis,
No cross-platform,
Overhead high,
Know the location of vulnerability
Machine learning,
Large search space problem

## Slide 64: BinSec
Automated vulnerability assessment of Mobile and IoT firmware
  To detect known security vulnerabilities
Assumptions (threat model):
  No source code access is available
  No cooperation from the device vendors
Success measures
  Accuracy: identify vulnerable/malicious code w/o false positives
  Performance: reasonable analysis time for practical deployments
  Usable: human-perceivable report generation about the discoveries

## Slide 66: BinSec’s Architecture
CFGs
Firmware Analysis and Feature Extraction
Vulnerable Code DB
(e.g., CVEs)
features
Deep Learning Neural Network Model Training
Preprocessing
(one-time)
binary
Feature Vector Calculation for All the Functions
Target Mobile/IoT Firmware Image Binary
vectors
Classification (whether vulnerable?)
Firmware
Static Analysis
traces
Dynamic Analysis of the Execution Traces
vectors
Trace-to-Trace Similarity Analysis to Discard False Positives
On-Device | Emulator-Based Execution of Reported Vulnerabilities
Dynamic
Analysis &
Reporting
Reports: vulnerable code points, sample exploits
1. Use A.I. and Machine Learning to Train the Vulnerability Detector
2. Vulnerability Detector analyzes the target Mobile/IOT firmware
3. The identified vulnerable components are run for verification!

## Slide 67: Binary Analysis
Subroutine Control Flow Graphs (of different ISAs, e.g., ARM, x86, etc.)
48-dimensional
feature vectors

## Slide 68: Deep Learning (one-time effort)
Goal: identify whether the following function pair come from the same (very similar) source codes (a CVE function binary, a firmware function binary)
  If so, the firmware function has the same vulnerability as the CVE function
Train a deep neural network to detect similar feature vectors
  Two similar feature vectors correspond to the two subroutine (function) binaries that come from the same (very similar) source codes
Training data: function pairs and a bit indicating whether the two functions are similar (each data point has 2x48+1=97 dimensions)
  (function-1 feature vector, function-2 feature vector, 0|1)
We generated >2,000,000 data samples for model training

## Slide 69: Deep Learning - Training (one-time effort)
>2,000,000 samples
Training (approx. 1 day)
96% accuracy

## Slide 70: How to locate vulnerable functions in a target Mobile/IoT firmware?

## Slide 71: Static Analysis of the TARGET Firmware
Firmware image
Control Flow Graphs
48-dimensional
feature vectors

## Slide 72: Static Analysis: Classification
CVE function
Classification (<2 seconds)
Similar
Non-similar
Firmware function
379 similarities
(vulnerable functions)
reported in Android i.e., 378 false positives

## Slide 73: How to identify and get rid of the false positives?

## Slide 74: Dynamic Analysis
Heavyweight analysis of the false positives, i.e., firmware functions reported as vulnerable by the static analysis
  Via concrete execution and comparison of the CVE and firmware functions
On-Device execution
  For Mobile/IoT devices where remote execution/debugging is feasible
  Our experiments: Android (Google Pixel 2 phone) and AndroidThings (LG Smart Display)
Emulator-based execution
  For closed IoT devices with limited/no dynamic access to its processor
  Our experiments: for non-Pixel (closed) Android phones
Steps
  Obtain the execution trace pairs of the false positives (subset of firmware functions and the corresponding CVE functions)
  Measure similarity of the trace pairs  report correct matches

## Slide 75: Dynamic Analysis (Challenges)
Execution
  The whole binary execution
  Function-level execution
How to do Function-level execution?
  DLOPEN
  Export all functions
Function inputs
  Fuzzing
Instrumentation
  GDB
  IDA PRO

## Slide 76: Dynamic Analysis
CVE function
Firmware function
On-Device or
Emulator-Based
Execution

## Slide 77: Dynamic Analysis
Trace2Trace Mapping (similarity calculation)
All false positives removed!
1 true positive identified.
Firmware function trace
CVE function trace
CVE trace features
Firmware trace features

## Slide 78: Case Study
CVE-2018-9412 (Android)
  This is a DoS vulnerability in the function removeUnsynchronization of the library libstagefright
  Android Things 1.0 firmware
Training dataset:
  100 Android libraries
  x86, amd64, ARM 32bit and ARM 64bit
  O0, O1, O2, O3, Oz, Ofast
  2,108 binary files
Some results
  5,646 functions
  252 candidate functions
  38 candidate functions

## Slide 79: Dynamic Features Vector Profiling

## Slide 80: Dynamic Features Vector Profiling
F_13: max frequency for the same branch instruction
F_14:max frequency for the same arithmetic instruction

## Slide 81: Calculating Function Similarity
Euclidean distance
Manhattan distance
Minkowski distance

## Slide 82: Evaluation
Dataset I
  100 Android libraries
  2,108 binary files
  2,037,772 function feature samples
Dataset II
  2,076 vulnerabilities (from 07/2016)
  1,351 high vulnerabilities and 381 critical vulnerabilities
Dataset III
  Android Things 1.0 and Google Pixel 2 XL (Android 8.0)
  25 different CVE vulnerabilities (Android 8.0 and 8.1)

## Slide 84: Outline
Introduction
Trace-free memory data structure forensics
Reversing semantics of embedded IoT software binaries
Case-study: data attacks against power system operations
Known vulnerability detection for Mobile/IoT firmware
Conclusion

## Slide 85: Conclusion
Recognize and recover data structure instances from a memory image without execution traces.
Locate the critical algorithm implementation and extract the semantic meaning for the associated memory addresses/registers.
Live memory semantic data attack against power system operations.
Leverage deep learning and dynamic analysis for semantic reverse engineering to do known vulnerability detection

## Slide 86: Acknowledgement
Thank my advisor Prof. Saman Zonouz who gave his extraordinary guidance, support, and encouragement throughout my entire PhD study.
Thank my committee members, Prof. Ivan Marsic, Prof. Wei Sheng and Dr. Praveen Murthy for their careful reading, insightful comments, and high standards.
Thank my family and friends for their incredible support throughout this entire chapter in my career.

## Slide 87: Publication List
I Know What You Didn't Do Last Vulnerability! Firmware Analysis via Deep Learning for Known Security Vulnerabilities Pengfei Sun, Luis Garcia and Saman Zonouz The 26th ACM Conference on Computer and Communications Security (CCS’19), to be submitted.
Tell Me More Than Just Assembly! Reversing Semantics of Embedded IoT and Industrial Control Software Binaries Pengfei Sun, Luis Garcia and Saman Zonouz The 49th IEEE/IFIP International Conference on Dependable Systems and Networks (DSN 2019), 2019.
Compromising Security of Economic Dispatch in Power System Operations Devendra Shelar, Pengfei Sun, Saurabh Amin, Saman Zonouz The 47th IEEE/IFIP International Conference on Dependable Systems and Networks (DSN 2017), 2017.
Trace-Free Memory Data Structure Forensics via Past Inference and Future Speculations Pengfei Sun, Rui Han, Mingbo Zhang, Saman Zonouz Annual Computer Security Applications Conference (ACSAC), 2016.
Power Grid Safety Control via Fine-Grained Multi-Persona Programmable Logic Controllers Gabriel Salles-Loustau, Luis Garcia, Pengfei Sun, Maryam Mehri, Saman Zonouz IEEE International Conference on Smart Grid Communications (SmartGridComm), 2017.
Cyber-Air-Gapped Detection of Controller Attacks through Physical Interdependencies Sriharsha Etigowni, Mehmet Cintuglu, Maryam Kazerooni, Shamina Hossain, Pengfei Sun, Katherine Davis, Osama Mohammed, Saman Zonouz IEEE International Conference on Smart Grid Communications (SmartGridComm), 2017.
Post-Intrusion Memory Forensics Analysis Pengfei Sun, Rui Han, Saman Zonouz Poster Session, The 37th IEEE Symposium on Security and Privacy (S&P), San Jose, CA, USA, May 23-25, 2016.
PLCloud: Comprehensive Power Grid PLC Security Monitoring with Zero Safety Disruption Henry Senyondo, Pengfei Sun, Robin Berthier, Saman Zonouz IEEE International Conference on Smart Grid Communications (SmartGridComm), Miami, USA, Nov. 2-5, 2015.
LBMS: Load Balancing based on Multilateral Security In Cloud Pengfei Sun, Qingni Shen, Ying Chen, Zhonghai Wu, Cong Zhang, Anbang Ruan, Liang Gu Poster session, The 18th ACM Conference on Computer and Communications Security (CCS’11), Chicago, USA, Oct. 17~21, 2011.
Thank You
Questions?
Email: pengfei.sun@rutgers.edu

## Slide 88: Backup

## Slide 89: Symbolic Execution
int main(int ac, char* av[]) {
int a = atoi(av[1]); //symbolic
int b = atoi(av[2]}; //symbolic
int c = atoi(av[3]}; //symbolic
if(a > b)
a = a – b;
if(b < 1) {
if(c != a)
c = a – b;
}
b = 1;
return 0;
}
Make variables (inputs) symbolic
Collect path constraints during execution
Solve path constraints by SMT solver  concrete values (test cases)
a > b
a = a - b
b < 1
b < 1
c != a
b = 1
c != a
b = 1
c = a - b
b = 1
c = a - b
b = 1
b = 1
b = 1
a <= b & b >=1
a <= b & b < 1 & c = a
a <= b & b < 1 & c != a
a > b & b >=1
a > b & b < 1 & c = a -b
a > b & b < 1 & c != a -b
Path Constraint
T
F
T
F
T
F
F
F
T
T

## Slide 90: PID

## Slide 91: Kalman Filter

## Slide 92: Application (orzhttpd)
08352000 0000 0000 00a9 0000 f039 574e 0010 0000
08352010 0001 0000 694c 756e 0078 0000 0000 0000
08352020 0000 0000 0000 0000 0000 0000 0000 0000
08352030 0000 0000 0000 0000 0000 0000 0000 0000
08352040 0000 0000 0000 0000 0000 0000 0000 0000
08352050 0000 0000 0000 0000 a870 bfb3 0050 0000
08352060 0118 0837 0138 0837 0158 0837 01b0 0837
08352070 0208 0837 0260 0837 0280 0837 02a0 0837
08352080 0308 0837 0000 0000 0036 0000 ace8 0804
08352090 af04 0804 2158 0837 22c8 0837 efef efef
083520a0 fefe fefe 00a0 0000 0000 0000 c409 0001
...
typedef struct {
time_t now; f039 574e
socklen_t salen; 0010 0000
unsigned int proc_num; 0001 0000
char sysname[SYS_NMLN]; 694c 756e +
const char *configfile; a870 bfb3
CONFIG_t config;
  typedef struct {
  uint16_t port; 0050 0000
  const char *user; 0118 0837
  const char *host; 0138 0837
  const char *basedir; 0158 0837
  const char *vhostbase; 01b0 0837
  const char *errmsgpath; 0208 0837
  const char *indexfile; 0260 0837
  const char *userdir; 0280 0837
  const char *accesslog; 02a0 0837
  const char *errorlog; 0308 0837
  const char *passfile; 0000 0000
  unsigned int options; 0036 0000
  } CONFIG_t
HTTP_STATE_t (*write)(CONN_t *); ace8 0804
void (*log)(LOG_TYPE_t, const char *); af04 0804
FILE *access_log; 2158 0837
FILE *error_log; 22c8 0837
} SERVER_t;
How can a semantic memory dump data structure layout provided by ReViver assist with detecting a non-control data attack?
Part of memory snapshot of orzhttpd

## Slide 93: Application (orzhttpd)
08370110 0000 0000 0021 0000 7777 2d77 6164 6174
08370120 ef00 efef feef fefe 15fe 0000 0000 0000
08370130 0000 0000 0021 0000 726f 2e7a 7962 6873
08370140 6e65 6e2e 7465 ef00 efef feef fefe 1bfe
08370150 0000 0000 0059 0000 0100 0000 2f65 6f64
08370160 2f70 6c66 776f 7473 7469 6863 612d 7474
08370170 6361 736b 6f2f 7a72 7468 7074 2f64 726f
08370180 687a 7474 6470 722d 6165 2d64 6e6f 796c
08370190 772f 7777 642f 7461 0061 efef efef fefe
083701a0 fefe 004e 0000 0000 0000 0000 0059 0000
083701b0 682f 6d6f 2f65 6f64 2f70 6c66 776f 7473
083701c0 7469 6863 612d 7474 6361 736b 6f2f 7a72
083701d0 7468 7074 2f64 726f 687a 7474 6470 722d
      The original root directory is “/home/orzhttpd/orzhttpd-read-only/www/data”
Part of memory snapshot of orzhttpd

## Slide 94: Live Memory Data Manipulation Attack
Memory structural pattern extraction
Sensitive region locator within the dynamic memory (through memory taint tracking)
Controller executable
Sensitive data source (e.g., sensors)
Logical graph-based memory pattern predicates
Binary code generation
Candidate memory addresses
Exploit
Instantiated object and member field data type reverse engineering
Extracted code and data pointers and their interdependencies
Memory vulnerability exploit

## Slide 95: Logical memory structural patterns
Intra-class type patterns
Code pointer-instruction patterns
Data pointer-based patterns
Intra-class
Fixed offset
Data types and/or values

## Slide 96: Logical memory structural patterns
Intra-class type patterns
Code pointer-instruction patterns
Data pointer-based patterns
Code segments read-only
Virtual function table
Virtual function prologue

## Slide 97: Logical memory structural patterns
Intra-class type patterns
Code pointer-instruction patterns
Data pointer-based patterns
Inter-object dependencies
Recursive pointer traversal
Direct graph