## Slide 1: Tell Me More Than Just Assembly! Reversing Cyber-physical Execution Semantics of Embedded IoT Controller Software Binaries
Pengfei Sun†, Luis Garcia∗ and Saman Zonouz† †Rutgers University, ∗University of California, Los Angeles
06/26/2019
The 49th IEEE/IFIP International Conference on Dependable Systems and Networks

## Slide 2: We live in a cyber-physical world…
* https://bricz.com/oms-integration/internet-of-thingsiot-and-cloud-computing-concept-smart-city-cyber-physical-systemscps/

## Slide 3: …and attacks are increasingly cyber-physical
Analyze and reverse engineer the system from security perspective

## Slide 4
int gcd(int a, int b){
int com_divisor;
if(b!=0){
com_divisor = gcd (b, a % b);
}
else{
com_divisor = a;
}
return com_divisor;
}
Compile and Link
Strip

## Slide 5: Reverse Engineering
Reverse Engineering
Assembly code
8048094: push ebp
8048095: mov ebp, esp
8048097: sub esp, 0x18
804809a: cmp [ebp + 0xc]:32, 0x0
804809e: jnz 0x80480a5
80480a0: mov eax, [ebp + 0x8]:32
80480a3: jmp 0x80480c1
80480a5: mov eax, [ebp + 0x8]:32
80480a8: mov edx, eax
80480aa: sar edx, 0x1f
80480ad: idiv [ebp + 0xc]:32
80480b0: mov eax, edx
80480b2: mov [esp + 0x4]:32, eax
80480b6: mov eax, [ebp + 0xc]:32
80480b9: mov [esp]:32, eax
80480bc: call 0x8048094
80480c1: leave
80480c2: ret
Decompiler
int32_t sub_8048094 (int32_t arg1, int32_t arg2){
int32_t eax1;
if(arg2!=0){
eax1=sub_8048094(arg2, arg1 % arg2);
}
else{
eax1=arg1;
}
return eax1;
}
???
Semantic information
Domain knowledge

## Slide 6
Decompiler
int32_t sub_8048094 (int32_t arg1, int32_t arg2){
int32_t eax1;
if(arg2!=0){
eax1=sub_8048094(arg2, arg1 % arg2);
}
else{
eax1=arg1;
}
return eax1;
}
infinityStoneCount
didWeLose
gauntLetFound

## Slide 7: Mismo: Domain-specific Reverse Engineering Framework
Propose a domain-specific reverse engineering framework to extract high-level algorithmic control- and data-flow semantics from embedded binary executables.
Introduce a semantic mapping using dynamic binary analysis and symbolic comparison of the mathematical and binary expressions to fill the semantic gap between high-level algorithm descriptions and low-level stripped binary segments.

## Slide 8: Domain Knowledge (Cyber-physical System)
Input
(sensor data)
Output
(actuation)
Control Algorithm
Pulse-width modulation (PWM)
Proportional-Integral-Derivate (PID)
Kalman-Filters

## Slide 9: Current Solutions
BinDiff (SSTIC'05)
BinJuice (PPREW '13)
Blex (Usenix’14)
Reward (NDSS’10)
TIE (NDSS’11)
Howard (NDSS’11)
ReViver (ACSAC’16)
IDA PRO
OllyDbg
Ninja
Snowman
Disassembler,
Decompiler,
Static and dynamic analysis
Data structure definition,
Data structure memory instance
Binary similarity checking
(Commercial or open source tools)

## Slide 10
Mismo Overview
Binary executable
Algorithm
ICS/IoT Device
Controller Code
(binary executable)
Control Algorithm’s Subroutine Identification
CFG Refinement
Symbolic Controller
Abstract Syntax Trees
ICS/IoT
Control Algorithms
Algorithmic Mathematical
Abstract Syntax Trees

## Slide 11
Algorithmic Mathematical
Abstract Syntax Trees
Formal Symbolic
Equivalence Check
Annotated
Disassembly
Mismo Overview
Symbolic Controller
Abstract Syntax Trees

## Slide 12
Mismo Overview
ICS/IoT Device
Controller Code
(binary executable)
Control Algorithm’s Subroutine Identification
CFG Refinement
Symbolic Controller
Abstract Syntax Trees
ICS/IoT
Control Algorithms
Algorithmic Mathematical
Abstract Syntax Trees
Formal Symbolic
Equivalence Check

## Slide 13
Case Study
ICS/IoT Device
Controller Code
(binary executable)
Control Algorithm’s Subroutine Identification
CFG Refinement
Symbolic Controller
Abstract Syntax Trees
ICS/IoT
Control Algorithms
Algorithmic Mathematical
Abstract Syntax Trees
Formal Symbolic
Equivalence Check
Chart: Functions
| sub_B7C8 | sub_9E14 | sub_A0C8 | sub_A020 | sub_9544 | sub_9288 | sub_9CA8 | sub_9BF8 | sub_8E10 | sub_8D68 | sub_8D68 | sub_9CA8 | sub_9BF8 | sub_8E10 | sub_8D68 | sub_8D68 | sub_8D68 | sub_8D68 | sub_10288 | sub_1024C | sub_94F8 | sub_8EC4 | sub_FBDC | sub_FBFC | sub_EB08 | sub_EB08 | sub_950C | sub_9158
Value_based Taint | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 15 | 0 | 15 | 15 | 0 | 0 | 0 | 0 | 0 | 0
Taint analysis
Arithmetic operations

## Slide 14
Case Study
ICS/IoT Device
Controller Code
(binary executable)
Control Algorithm’s Subroutine Identification
CFG Refinement
Symbolic Controller
Abstract Syntax Trees
ICS/IoT
Control Algorithms
Algorithmic Mathematical
Abstract Syntax Trees
Formal Symbolic
Equivalence Check
14
Errors checking,
Value range checking

## Slide 15
Case Study
ICS/IoT Device
Controller Code
(binary executable)
Control Algorithm’s Subroutine Identification
CFG Refinement
Symbolic Controller
Abstract Syntax Trees
ICS/IoT
Control Algorithms
Algorithmic Mathematical
Abstract Syntax Trees
Formal Symbolic
Equivalence Check

## Slide 16
Backward value analysis
Case Study
Symbolic Controller
Abstract Syntax Trees
Symbolic expression
Symbolic execution
Symbolic
output
variable
Symbolic
input
variables
…
0x90DE: VMUL.F64 D6, D6, D7
-> 0xc0175999f54482ee
0x90E2: VLDR D7, [R7,#0x3C+var_2C]
-> 0x4028000000000000
0x90E6: VADD.F64 D7, D6, D7
-> 0x4018a6660abb7d12
…
Backward slicing analysis

## Slide 17
Case Study
Symbolic Controller
Abstract Syntax Trees
Symbolic expression
(for Kalman filter – obtained by symbolic execution of the controller binary file)
((((Sym_15 ∗ (((Sym_12 ∗ Sym_11) ∗ Sym_13) + Sym_14)) / ((Sym_19 ∗ (Sym_15 ∗ (((Sym_12 ∗ Sym_11) ∗ Sym_13) + Sym_14))) + Sym_16)) ∗ ((((Sym_7) ^ (-1) ∗ Sym_8) + ((Sym_5 ∗ (((Sym_3) ^ (-1) ∗ Sym_4) + ((Sym_0 ∗ Sym_1) + (Sym_18 ∗ Sym_2)))) + (Sym_18 ∗ Sym_6))) − ((Sym_19 ∗ ((Sym_18 ∗ Sym_10) + (Sym_11∗ Sym_9))) + (Sym_17 ∗ Sym_18)))) + ((Sym_18 ∗ Sym_10) + (Sym_11 ∗ Sym_9)))

## Slide 18
Case Study
Symbolic Controller
Abstract Syntax Trees
(obtained from the controller binary files)

## Slide 19
Case Study
Algorithmic Mathematical
Abstract Syntax Trees
(obtained from the control algorithm)

## Slide 20
Formal Symbolic
Equivalence Check
Mismo Overview
Sym_3 -> Q
Sym_7 -> R
…

## Slide 21: Annotated Disassembly

## Slide 22: Evaluation
Accuracy
Data: the portion of resolved symbolic variables
Code: the portion of resolved instructions

## Slide 23: Evaluation

## Slide 24: Potential Use-cases

## Slide 25: Potential Use-cases
Binary vulnerability assessment

## Slide 26: Potential Use-cases
Binary vulnerability assessment
Memory forensics analysis

## Slide 27: Potential Use-cases
Binary vulnerability assessment
Memory forensics analysis
Sensitive code and data segment protection

## Slide 28: Potential Use-cases
Binary vulnerability assessment
Memory forensics analysis
Sensitive code and data segment protection
Correct algorithm implementation verification

## Slide 29: Potential Use-cases
Binary vulnerability assessment
Memory forensics analysis
Sensitive code and data segment protection
Correct algorithm implementation verification
Binary-level software similarity measures

## Slide 30: Comparison with Snowman (decompiler)

## Slide 31: We Discovered/reported a Linux Kernel Bug
…
/* compute intermediate PID terms */
p_term = -p_param.kp * (xk - xk_1);
i_term = p_param.kp * p_param.ki * p_param.ts * ek;
d_term = -p_param.kp * p_param.kd * (xk - 2 * xk_1
+xk_2) / p_param.ts;
/* compute output */
*yk += p_term + i_term + d_term;
…
Mismo
Algorithm
Program Code

## Slide 32: Attack Control Algorithm Parameter

## Slide 33: Conclusions & QA
A general framework to extract semantic information of an embedded firmware binaries with respect to its associated high-level control algorithm.
Using dynamic binary analysis and symbolic comparison of the mathematical and binary expressions to fill the semantic gap between high-level algorithm descriptions and low-level stripped binary segments.
Thank You
Questions?
Email: pengfei.sun@rutgers.edu